## Slide 1: Materials, Level 1 (Health)
Level 1 Minimum Requirements | GreenGuard Gold Certified Products | All the following product categories shall be GreenGuard Gold Certified, or an approved equivalent (see GreenGuard Gold Equivalency Guide for a list of approved equivalent certifications): Interior Architectural Adhesives and Sealants (unless a project team can demonstrate that no compliance product is available for a specific adhesive/sealant application in a specific region Carpet and Flooring Adhesive Carpet Resilient Flooring and Baseboard (Vinyl, Linoleum, Laminate, Rubber, Cork) Ceiling Tiles Drywall Interior Paints Dry-erase Paint Spray Polyurethane Foam (SPF) Insulation - and must contain no chlorofluorocarbons Fiberglass Insulation Furniture – Global Standards* *Note: Ancillary Furniture is recommended to meet GreenGuard Gold Certification.
Notes: Key Fact, then...
The requirement for Level 1 is that a given list of materials must be GreenGuard Gold certified. But why Greenguard Gold?
-GREENGUARD Gold offers some of the world's most rigorous and comprehensive standards for low emissions of VOCs into indoor air which can be a major source of indoor air pollution and may contribute to health problems uch as asthma and allergies. Products carrying the seal have been tested for over 10,000 chemicals and more than 360 VOCs and certified as low-emitting by this independent, trusted 3rd party. This standard is seen around the globe and built in to global rating systems such as LEED and WELL, so using this third-party standard will make product compliance evaluation a straightforward process.
-Most of the products MSFT buys is compliant with GGG, and we are currently working on vetting materials and working with manufacturers to ensure compliance.
- currently working with our carpet and furntiure suppliers to pre-vet materials and that while ancilary furnture is not required to meet the standard, it is highly recommended.
-The central sustainability team is available to support this effort but that product vetting is the responsibility of the architect, gc and PM

## Slide 2: Materials, Level 1 (Health)
Level 1 Minimum Requirements | Wood Floors | All wood floors shall contain no added formaldehyde (NAF) and ultra-low emitting formaldehyde-based resins (ULEF). This shall be documented by a letter of confirmation from the manufacturer. *Note: For laminate or engineered wood, see the requirement for Resilient Flooring
 | Millwork | Except reclaimed wood, all millwork shall contain no added urea formaldehyde (NAUF). This shall be documented by a letter of confirmation from the manufacturer.
 | Composite Wood | All composite wood products, including hardwood plywood, particle board, and medium density fiber board shall contain no added urea formaldehyde (NAUF). This shall be documented by a letter of confirmation from the manufacturer.
1. Advantages of FSC. https://us.fsc.org/en-us/what-we-do/advantages-of-fsc
Notes: Focusing on wood products and their health implication, the main exclusion here is fomaldehyde in its various forms.
-Wood Floors must be NAF and ULEF resins
-Millwork and composite wood (particleboard, MDF, plywood, etc.) must be NAUF

## Slide 3: Materials, Level 2 (Leadership)
Level 2 Minimum Requirements | Wood Floors and Millwork | All permanently installed wood shall be either reclaimed wood or certified by the Forest Stewardship Council (FSC). Small exceptions may be made if FSC-certified products are unavailable in some regions, but for all projects, at least 50% of permanently installed wood should comply with this requirement.
 | LEED BPDO – Sourcing of Raw Materials Credit | Meet Option 2 of the LEED "Building product disclosure and optimization - sourcing of raw materials" credit: Leadership Extraction Practices or the prescriptive recycled content criteria for the materials below.
 | Ceiling tiles | Specify 25% post-consumer recycled content Collect Environmental Product Declaration (EPD) - Product Specific Type III EPD
 | Gypsum Board | Collect Environmental Product Declaration (EPD) - Product Specific Type III EPD
 | Carpet | Specify 30% pre-consumer recycled content Specify 5% post-consumer recycled content OR 5% bio-based material content Collect Environmental Product Declaration (EPD) - Product Specific Type III EPD
 | Aluminum | Specify 25% post-consumer recycled content Collect Environmental Product Declaration (EPD) - Product Specific Type III EPD
 | Concrete | Specify 50% pre-consumer recycled content for foundations and topping slab Specify 25% pre-consumer recycled content for vertical applications Collect Environmental Product Declaration (EPD) - Product Specific Type III EPD
 | Glass/ Glazing | Collect Environmental Product Declaration (EPD) - Product Specific Type III EPD
Notes: Moving on to Level 2 requirements,
-All PERMANENTLY installed wood, so wood floors and permanently installed millwork must be FSC
-Why FSC: it reduces the risk of fires, prevents deforestation, preserves biodiversity, helps mitigate climate change, and preserves water and soil…the list goes on.
-Beyond that, products must also meet given recycled content and material transparency requirements. For recycled content, a project team has two options:
-1. Meet the LEED credit Building Product Disclosure and Optimization – Sourcing of Raw Materials” – this gives product teams flexibility to achieve leadership extraction practices such as increased recycled content or use of bio-based materials for 25% of the project’s overall materials costs.
-OR 2. meeting the prescriptive recycled content percentages for ceiling tiles, gyp board, carpet, aluminum, concrete and glass as outlined below. These percentages are based on global industry research that we’ve done to verify what’s achievable in various parts of the world.
-In addition to recycled content, products within those same categories – ceiling tiles, gypsum board, carpet, aluminum, concrete and glass – must have an Environmental Product Declaration – or EPD.
-An EPD is basically like the environmental nutrition label for a product – it describes the life-cycle from start to finish and its impact on the environment. It doesn’t say a product is better or worse than another one, but it gives us the information that helps us make that determination.

## Slide 4: Materials, Level 3 (Carbon)
Level 3 Minimum Requirements | Embodied Carbon | All projects must develop a strategy at project concept phase to reduce embodied carbon from project life cycle. Engage with Microsoft Sustainability Lead at early design stages (concept or schematic design) to develop a project specific strategy to reduce embodied carbon. Best-practices for embodied carbon reduction includes the assessment of embodied carbon of building materials through: Optimizing high-embodied-carbon system within a building (e.g. structural systems, envelope systems, finishes and etc) and substituting those material systems with low-embodied-carbon options. The AIA Materials Matter is a great resource. Assessing embodied carbon with a whole-building life-cycle assessment (WBCLA). This method uses an LCA software and data base to evaluate carbon emissions of building materials taking into account from extraction, to manufacturing, to end-life of building materials such as, concrete, cement, steel, wood, gypsum and etc. The Carbon Leadership Forum includes a guide on LCA and is about to release an LCA software. When not available on a material data base the embodied carbon of specific material can be found at an Environmental Product Declaration (EPD). An EPD consist of an LCA of specific products, rather than an entire building.
1. Architecture 2030. https://architecture2030.org/new-buildings-embodied/
Notes: And lastly, Level 3 focuses on embodied carbon.
-Embodied carbon is the measure of how much CO2 is emitted throughout a product’s life-cycle: so, extraction of the materials, manufacture, transportation to the project site, installation, use, and end-of-life.
-As green building professionals, we have historically focused on the carbon emitted on a project site, but we’ve neglected the carbon emitted in the process of getting materials to the site, which is actually about 50% of the total emissions. That’s huge! That’s why it’s critical to tackle this parameter now.
-For this requirement, projects must develop a strategy to reduce embodied carbon from the project life-cycle in concert with Microsoft Susty Lead in the early design stages.
-Resources include the newly released EC3, which [INCLUDE BLURB ABOUT EC3 HERE]